## Slide 1
5G Signaling Network Solution
Signaling Network Change To Towards 5G
Nchf
SCP
BSF
DRA
CloudSPS
HSS
PCRF
OCS
IMS
EPC
5GC
CHF
UDM/AUSF
Gy
S6a/Cx/Sh
Gx/Rx
Sh
S6a/Gx/Gy
N8/N12/N15
PCF
Nchf
N7/N8/N12/N15
N7/N15/Nbsf
Diameter
Diameter
Diameter
HTTPS
CloudSPS = DRA + SCP + BSF
5GC
PCC
EPC
IMS
Huawei Cloud Signaling Service Processing System (CloudSPS) converges the Diameter Routing Agent (DRA), Binding Support Function (BSF), and Service Communication Proxy (SCP) functions and routes 4G&5G signaling within a PLMN.
CloudSPS with the SCP and DRA co-located:
Supports 4G&5G routing data sharing.
Defends against network-level traffic surges and dispatches traffic in real time for load balancing.
CloudSPS with the BSF and DRA co-located:
Supports 4G&5G session binding data sharing, reducing database resource consumption.
Reduces 4G-5G interactions, simplifying the session binding data query process.
4G
5G NSA
5G SA
MME+/AMF
P-GW+/SMF
Maximizing 4G signaling network investment returns
Supports the smooth evolution to 5G.
Accelerating 5G network construction
Supports 4G&5G session binding data sharing and reduces overlapping configurations.
Uniformly monitors 4G&5G signaling and identifies signaling attacks.
Migrating the DRA and DEA to the cloud
Upgrading software to support 5G NSA deployment
Evolving to support 5G SA deployment based on the SBA
DRA+&SCP
DEA+&SEPP
Other networks
Diameter
Diameter
Diameter & HTTP
Diameter & HTTP
Diameter
Diameter
Other networks
Other networks
Safeguarding signaling
VoLTE
PCRF
HSS
MME
P-GW
VoLTE
PCRF+
HSS+
MME+
P-GW+
DRA
DEA
DRA+
DEA+
VoLTE/Vo5G
PCRF+/PCF
HSS+/UDM

## Slide 2
5G Signaling Network Solution
Region A
HSS/UDM
/AUSF
Region B
Region A
Region B
PCRF/PCF
OCS/CHF
NRF
MME/AMF
PGW/SMF
AF
HSS/UDM
/AUSF
PCRF/PCF
OCS/CHF
MME/AMF
PGW/SMF
AF
NRF
HSS/UDM
/AUSF
PCRF/PCF
OCS/CHF
NRF
SCP
MME/AMF
PGW/SMF
AF
HSS/UDM
/AUSF
PCRF/PCF
OCS/CHF
MME/AMF
PGW/SMF
AF
SCP
NRF
The CloudSPS provides the SCP functions to converge HTTP signaling. This simplifies network topology and facilitates O&M.
SCP Functions
SCP Deployment Scheme
SCP A
SCP B
N7
AMF
PCF
UDM
N8
N7
N40
N40
N15
N15
N10
AUSF
N12
SBI
NRF
Nnrf
SMF
CHF
SCP A
C link
SCP B
Physical link set
Signaling flow
NF service producer 1
NF service producer 2
NF service consumer 1
NF service consumer 2
N8 N10
N12
The SCP provides the following functions:
Signaling aggregation: It converges signaling to simplify a mesh network to a star network.
Flexible message routing: It provides flexible routing policies, such as routing messages based on FQDNs, subscriber identities, or IP addresses in URIs.
Delegated NF discovery: It is delegated by the NF service consumers to initiate service discovery with the NRF.
SCPs are deployed in pairs for redundancy. SCPs in a pair (SCP A and SCP B) share traffic load with each other and communicate over C links. If the HTTP link between SCP A and an NF becomes faulty, SCP A forwards messages to SCP B over C links. SCP B then forwards the messages to the target NF. This enhances service reliability.

## Slide 3
5G Signaling Network Solution
Interactions with the NRF: The BSF registers, updates, or deregisters its NF profile with the NRF.
Interactions with the PCF: The PCF registers or deregisters session binding information with the BSF.
Interactions with the NEF/AF: The NEF/AF invokes the Nbsf_Management service to query session binding information for the PCF address.
Interactions with the P-CSCF: The BSF receives AAR messages from the P-CSCF over the Rx interface.
BSF
NRF
P-CSCF
PCF
NEF/AF
HTTP/Nnrf
HTTP/Nbsf
HTTP/Nbsf
Diameter/Rx
Interface | NF/NE | Service Process | Protocol
Nnrf | BSF -> NRF | NF profile registration Nnrf_NFManagement_NFRegister | HTTP/2.0
 |  | NF profile update Nnrf_NFManagement_NFUpdate | 
 |  | NF profile deregistration Nnrf_NFManagement_NFDeregister | 
Nbsf | BSF <- PCF | Session binding information registration Nbsf_management_Register | 
 |  | Session binding information deregistration Nbsf_management_Deregister | 
 | BSF <- NEF/AF | Session binding information query Nbsf_management_Discovery | 
Rx | BSF <- P-CSCF | Session binding information query | Diameter
The CloudSPS provides the 3GPP-compliant BSF functions. The BSF facilitates target PCF addressing on a 5G network.
If multiple PCFs are deployed on a 5G network, the BSF queries session binding data for the PCF serving a subscriber, such as the IP address or DNN. Afterwards, it sends the PCF information to the NEF or AF. The NEF or AF then can route messages received from the subscriber over different interfaces (N7, N5, and Rx) to the target PCF during data and voice services.
BSF Functions
Interactions with NFs/NEs

## Slide 4
5G Signaling Network Solution
5G voice services are still provided by the IMS network. To support VoNR services for 5G subscribers, the BSF needs to be able to interwork with the DRA on the IMS network over the Rx interface. The BSF can act as a proxy agent or a redirect agent to help the DRA address a PCF, as defined in 3GPP TS 29.513.
Proxy agent: After receiving an AAR message from the DRA, the BSF obtains the host name of the target PCF, includes the PCF host name in the AAR message, and sends the message to the target PCF over the Diameter link.
Redirect agent: After receiving an AAR message from the DRA, the BSF obtains the host name of the target PCF and returns a response carrying the PCF host name to the DRA. The DRA then redirects the AAR message to the target PCF.
When the BSF acts as a proxy agent, Diameter links between the BSF and PCF are required.
When the BSF acts as a redirect agent, Diameter links between the BSF and PCF are not required.
Deployment Scheme
Here is a recommended scheme when a standalone BSF is deployed.
In this scheme, it is recommended that dedicated IP segments be allocated to 5G subscribers during attach procedures to help the DRA distinguish 5G subscribers from 4G.
NF/NE | Deployment
BSF | Deploy two BSFs as an active/active pair and each BSF connects to multiple PCRFs.
DRA | Add Diameter links for the BSF to interwork with the DRA. If IP addresses in Rx messages fall in the IP segments dedicated for 5G subscribers, the DRA queries the BSF over Diameter links.
PCF | Deploy the BSF to interwork with the PCF over HTTP and Diameter links.
NRF | Deploy the BSF to interwork with the NRF over HTTP links.
NEF/AF | Deploy the BSF to interwork with the NEF/AF over HTTP links.
BSF Deployment Scheme
DRA
PCF
PCF
NRF
…
BSF
HTTP link
Diameter link
DRA
NEF/AF
Redirect
Proxy
NR
SMF
IMS AF
Rx
N7
5G Core
IMS
BSF
Rx
Sends an AAR message.
02
01
AMF
UE
PCF 1
PCF 2
PCF 3
DRA
Returns a redirection indication.
05
Sends the AAR message to the target PCF.
04
03
04
Applies for QoS policies.
Sends the AAR message to the target PCF.
Registers binding information.
BSF
The BSF is configured to interwork with the DRA over Diameter links.
The DRA on the live network remains unchanged.